## Slide 1: Simulated Dataset for the Loaded vs. Unloaded UAV Classification Problem Using Deep Learning
Hamid Azad*, Varun Mehta, Miodrag Bolic*, Iraj Mantegh
* University of Ottawa
 National Research Council Canada (NRC)

## Slide 2: Contents
Introduction
Simulated dataset using AirSim
    Statistics about the dataset
Loaded vs. unloaded drone classification problem
Simulation results
Conclusion

## Slide 3: Introduction
Uncrewed or Unmanned Aerial Vehicles (UAVs), also known as drones, and their vast usage in various applications
Serious concerns about safety and security issues such as transporting smuggled goods and other illegal substances
The necessity of addressing the loaded vs. unloaded drone classification problem

## Slide 4: Introduction
Various sensors to detect the drone’s payload
    Radar: using micro-Doppler signature
    Acoustic: using Mel-Frequency Cepstral Coefficients (MFCC)
    Vision Camera
      Several advantages, including affordability, compact implementation, and lower power consumption
      Deep learning-based classifiers and the necessity of having a huge amount of data
      Data through real tests is costly and time-consuming
      Simulation is the solution! Providing controlled condition
j

## Slide 5: Simulated dataset using AirSim
AirSim: an open-source simulation tool developed by Microsoft, that enables the simulation of drones and cars in diverse environments.
    Only one simple quadcopter available as the default model
    Importing several types of drones into AirSim
      Preparing the 3D model in Autodesk Maya
      Five types of drones are imported: DJI Phantom, DJI Mavic, DJI Inspire, DJI FPV, Quadrotor
    Considering several types and colors of payload

## Slide 6: Simulated dataset using AirSim
AirSim: an open-source simulation tool developed by Microsoft, that enables the simulation of drones and cars in diverse environments.
    Several environments and backgrounds for dataset diversity
      The Blocks environment: the simplest case with a primarily sky background, except when the drone is near the blocks
      The Landscape Mountains environment provides a natural setting with trees, rocks, and a lake in the background
      The City Park environment offers a blend of natural elements, such as trees, along with man-made objects like buildings. By simulating various backgrounds

## Slide 7: Simulated dataset using AirSim
Dataset specification
Some samples

## Slide 8: Loaded vs. unloaded drone classification
Potential to define several problems on the developed dataset
    Loaded-vs-unloaded drone binary classification just for a single type of drone
    Loaded-vs-unloaded drone classification for the general case of several drone models in the dataset
    Classification among various payload forms for the single and/or multiple types of drones (unloaded vs. loadedattached vs. loadedhanging)
ResNet-34 as the classifier to address the problem
    34-layer deep convolutional neural network in the category of residual networks
    Residual architecture to address the gradient vanishing problem in training
    Structure inspired by the famous VGGnet architecture

## Slide 9: Simulation results
Several cases in the simulated dataset
    Splitted data into 70%, 15%, and 15% for the training, validation, and test sets
    Number of epochs: 25
    Batch size: 64
    Learning rate: 0.03

## Slide 10: Simulation results
Verification using the practical data
    Trained data on the simulated dataset
    A quadrotor flying at various distances (from 20 to around 100 meters) from the camera
    Box-shaped payload (with dimensions of 7.8 × 9 × 15cm3) was attached underneath the drone
    Camera resolution: 1080×1920 pixels
    Average occupied pixels by the drone: 20 pixels
    Classification accuracy of 98% and 97% for the unloaded and loaded cases
    Sample frames for the loaded (up), and unloaded (bottom) cases

## Slide 11: Conclusion
The first synthetic dataset specifically designed for the loaded vs. unloaded drone classification
Developed dataset using AirSim:
    Incorporating diverse types of drones, environments, payloads, and weather conditions
Using ResNet-34 deep network to address several classification problems within the dataset.
Real-world drone classification: Promising results with the trained network from simulated data
Practical payload detection results confirmed the effectiveness of the synthetic dataset

## Slide 12: THANK YOU
Any question?